## Slide 1: sulfate-free surfactants meeting trends, technologies and formulating expertise
Susan Pye InterCharm Conference, September 2019

## Slide 2: product claims: a rise in sulfate-free
shampoo and skin cleansers, Mintel 2019
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Europe | 384 | 442 | 480 | 517 | 667 | 827 | 950 | 1031 | 1359 | 401
Asia Pacific | 136 | 204 | 178 | 184 | 288 | 422 | 474 | 670 | 911 | 178
North America | 288 | 331 | 298 | 228 | 448 | 309 | 462 | 608 | 591 | 188
Latin America | 68 | 39 | 21 | 57 | 57 | 125 | 156 | 190 | 245 | 63
Middle East & Africa | 10 | 29 | 23 | 22 | 25 | 45 | 65 | 113 | 124 | 31

## Slide 3: Innospec sulfate-free portfolio
Type | Product name
SLMI | Iselux® range
SCI | Pureact I-series
Taurates | Pureact WS range Pureact TR-L90 *NEW*
AOS | Nansa® range
CAPB | Empigen® BS/FA and BS/H50
APG/Lactylate | Pureact 138 *NEW*
Primary Surfactants
Selection based on formulation pH,
cost, naturalness
Type | Product name
CAPB | Empigen® BS/FA and BS/H50
Alkyl Betaine | Empigen® BB and CBET
Amphoacetates | Empigen® range
Sarcosinate | Pureact LSR
Taurates | Pureact WS, MS range Pureact TR-L90 *NEW*
Glycinates | Pureact SLG, Pureact SCG
APG | Pureact Gluco range
APG/Lactylate | Pureact 138 *NEW*
Secondary Surfactants
Selection based on viscosity and foam/
texture /application
Electrolytes (NaCl, NH4Cl) | Low cost
PEG esters | Clarity
Cocamide (Empilan® series) | High/low shear viscosity
Polymers | Suspension, clarity
Thickeners
Selection based on several parameters
Type | Product name
Cationic Guars | Activsoft range
Cationic Polymers | PQ10, PQ7, PQ37, PG22
Amido amines | Empigen® S18
Silicones & Derivatives | Innospec speciality silicone range
Conditioning
Selection based on several parameters
We also have expertise in formulating in combination with non-Innospec surfactants

## Slide 4
Popular Sulfate-Free Anionic Surfactants | pH Stability Range
Sodium Lauroyl Methyl Isethionate (Iselux®) | 5.0 – 9.0
Sodium Cocoyl Isethionate (Pureact I-series) | 6.0 – 8.5
Sodium Lauryl Sulfoacetate | 6.0 – 8.5
Sodium Laureth Sulfosuccinate (Empicol® SDD/O) | 6.0– 8.5

## Slide 5
Popular Sulfate-Free Anionic Surfactants (Continued) | pH Stability Range
Sodium Methyl Cocoyl Taurate (Pureact WS) | 3.0 - 11.0
Sodium Lauroyl Sarcosinate (Pureact LSR) | 3.0 - 11.0
Sodium C14-C16 Olefin Sulfonate (Nansa® LSS) | 3.0 - 11.0

## Slide 6
Optimum pH ranges of Innospec Surfactants
pH range for organic acid preservatives efficacy
5
6
7
pH
4
8
9
Iselux®
(Sodium Lauroyl Methyl Isethionate)
Pureact I Grades
(Sodium cocoyl Isethionate)
Pureact Gluco Grades (Alkyl Glucosides)
Pureact WS & MS Grades
(Sodium Methyl Alkyl Taurates)
Nansa® LSS Grades
(Sodium C14-C16 Olefin Sulfonate)
Pureact SCG
(Sodium Cocoyl Glycinate)
Pureact LSR (Sodium Lauroyl Sarcosinate)
Low solubility in acid form
Empicol® SDD/O (Disodium Laureth Sulfosuccinate)
Amphoacetates & Betaines

## Slide 7: Stability Issues Surfactant Hydrolysis in Formulations at Acidic pH
Loss of clarity
In clear systems due to break down into insoluble fatty acids
Can be masked with pearlisers (but gives additional cost and also a need for stabilisation of the pearliser)
Change in viscosity
Due to depletion of surfactant
Normally shows initial increase with low levels of fatty acid then rapid drop in viscosity as surfactant level drops and rate of hydrolysis increases due to auto catalysis. Can be masked with rheology modifiers which don’t rely on surfactants to thicken, e.g. carbomers, xanthan, cellulose gums
Loss in foam performance
Reduction in flash and total foam volume
Depletion of surfactant gives a reduction in flash and total foam volume. Can be masked by deliberately overloading the surfactant levels. But at additional cost!
Instability
With fragrances and oils

## Slide 8: Iselux® INCI: Sodium Lauroyl Methyl Isethionate
Features
Benefits
Dense creamy lather
High flash foam
Mild surfactant, low irritation
Excellent water solubility
Easy to handle forms
High concentration flake
Cold process liquid
Surfactant concentrates
Readily biodegradable
Naturally derived
pH stability 5.0 - 9.0
Viscosity build with CAPB
Ideal for sensitive skin
Can be used easily in clear systems
Creates a luxurious bath / shower
experience
Formulating flexibility
Organic acid preservative compatibility
Ease of manufacturing
Dramatic formulation flexibility
Environmentally friendly

## Slide 9: Product Launches with Iselux® INCI: Sodium Lauroyl Methyl Isethionate
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Europe | 21 | 50 | 54 | 57 | 76 | 114 | 115 | 220 | 58
North America | 17 | 16 | 33 | 30 | 26 | 45 | 87 | 109 | 31
Asia Pacific | 13 | 5 | 10 | 12 | 17 | 25 | 42 | 84 | 17
Latin America | 1 | 1 | 11 | 27 | 23 | 10 | 11 | 25 | 4
Middle East & Africa | 1 | 0 | 0 | 0 | 1 | 5 | 16 | 11 | 6
Data from Mintel 2019

## Slide 10: Pureact WS Series INCI: Sodium Methyl Cocoyl Taurate Pureact MS Series INCI: Sodium Methyl Oleoyl Taurate
Features
Benefits
Mild surfactant, low irritation
High Foaming in the presence of
oil and sebum
Powder (>70% active)
Paste (30% active)
Mobile Liquid (22% active)*
Readily biodegradable
Derived from natural resources
Wide pH stability 3.0 - 11.0
Mixed foam profile,
Large and small bubbles
Ideal for sensitive skin
High oil cleansing formulations
Sebum removal anti acne
Creates a luxurious bath / shower
experience
Ease of handling in manufacturing
Extreme pH formulations possible
Feminine hygiene, anti acne treatments, fatty acid soaps
* Unique to Innospec Pureact WS-70
Environmentally friendly

## Slide 11: Product Launches with Sodium Methyl Cocoyl Taurate
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Asia Pacific | 174 | 236 | 250 | 293 | 417 | 126
Europe | 84 | 100 | 96 | 111 | 260 | 54
North America | 86 | 64 | 83 | 99 | 130 | 28
Latin America | 3 | 2 | 18 | 16 | 31 | 12
Middle East & Africa | 7 | 10 | 14 | 9 | 7 | 7
Data from Mintel 2019

## Slide 12
High foaming sodium chloride-free, mild, anionic, solid flake surfactant.
Suitable as a primary or secondary surfactant.
No NaCl - more suitable for applications such as toothpastes and other oral care products.
Starting formulations available.
Pureact TR-L90
INCI: Sodium Methyl Lauroyl Taurate
New product launch

## Slide 13: Nansa® LSS Series INCI: Sodium C14-C16 Olefin Sulfonate
Features
Benefits
High foaming with oils
Powder (80% active)
Mobile liquid (28% active)
Readily builds viscosity
with amphoteric surfactants
Wide pH stability: 3.0 - 11.0
Mixed profile large/small bubbles
Readily biodegradable
Creates a luxurious bath / shower
experience
Ease of handling in manufacturing
Extreme pH formulations possible
Cost effective
High oil cleansing formulations
Sebum removal anti acne
Environmentally friendly
Formulating flexibility

## Slide 14
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Asia Pacific | 104 | 145 | 143 | 182 | 214 | 51
Europe | 85 | 112 | 122 | 128 | 271 | 59
North America | 110 | 88 | 124 | 197 | 165 | 61
Latin America | 42 | 70 | 82 | 95 | 122 | 20
Middle East & Africa | 13 | 22 | 38 | 39 | 36 | 10
Product Launches with Sodium C14-16 Olefin Sulfonate
Data from Mintel 2019

## Slide 15: Pureact 138 INCI: Decyl Glucoside (and) Sodium Lauroyl Lactylate
Mild and rich creamy foaming.
Suitable as a primary or secondary surfactant blend.
Cold processable.
Usage level - 2 – 30%
Preservative free.
Both components are derived from natural, readily renewable resources. (100% naturally derived)
Recommended for hand soap, body wash, shampoos, facial cleansers and “natural” products.
Starting formulations available.
New product launch

## Slide 16: formulating sulfate-free considerations
Specific application
Sulfate-free surfactants can produce a wide variety of foam textures They have different levels of compatibility with cationics used as conditioning agents Some are thus more suitable for use in skin/facial cleansers and others have better performance in hair care applications
Target pH
SLS and SLES have broad pH stability range Suitable pH ranges can be narrower for some sulfate-free surfactant technology, based on their chemistry (e.g esters or amides) Low pH systems (< pH 5) are frequently required for organic acid preservation
Level of natural ingredient claim
Possibility to use synthetic/petrochemical products based on claim, required mildness, and cost, performance targets Percentage naturally derived requirements following ISO16128-1&2 or other standards/ natural % calculations Cosmos/Ecocert approved material requirements
Target viscosity
Viscosity build from surfactants and electrolytes alone? Other claim requirements for the thickening system (Natural, EO free, Acrylate free)? Particle suspension or emulsion stabilisation required?

## Slide 17: formulating sulfate-free considerations (continued)
Transparency
Crystal clear or translucent formulation Opaque or pearlised, suspension stabilisation of particles yield
Texture
Texture : cream, butter, lotion, gel Packaging type: bottle, tube, pot
Additives
Incorporation of fragrance, oils, actives, silicones e.g. PEG-X hydrogenated Castor Oils and Polysorbate 20 significantly depress viscosity build with sulfate free will need rheology modifiers Polyglyceryl-X based emulsifiers have much lower negative impact on viscosity e.g. Tego Solv 61
Other considerations
Cold process manufacturing Formulation cost Formulation globally compliant Mildness

## Slide 18: 10% w/w Active Iselux® + Cocamidopropyl Betaine (pH 6.0) Viscosity Brookfield RVT, 20rpm # 2, 3, 4 and 5
NaCl / % w/w
Viscosity / cps 20°C
6% Active Betaine (oil based)
4% Active Betaine (oil derived)
2% Active Betaine (oil derived)
0% Betaine
2% Active Betaine (Empigen® BS/FA)
A binary system using Iselux® + betaine increased formulation viscosity
Topped fatty acid betaines provide increased viscosities at lower concentrations vs. oil based betaines
Electrolyte Thickening of Iselux®/CAPB Systems
4% Active Betaine (Empigen® BS/FA) (stripped fatty acid based)
Choice of CAPB grade is important: Stripped/topped fatty acid based CAPBs give the highest viscosity compared to triglyceride oil based CAPBs

## Slide 19
Chart: NaCl / % w/w
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Empigen BS/FA | 0 | 0 | 0 | 0 | 135 | 340 | 840 | 1850 | 3380 | 5380 | 7390
CAPB A | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 50 | 290 | 580
CAPB B | 0 | 0 | 0 | 0 | 0 | 20 | 150 | 250 | 480 | 905 | 1540
(Oil derived )
(~30% Active)
(Hardened Oil derived CAPB)
(~38% Active)
(Fatty Acid Based (Topped) (~30% Active)
6% Active Sodium Methyl Cocoyl Taurate, 4% Active Cocamidopropyl Betaine, pH 5.0
Viscosity Brookfield RVT, 20 rpm # 2, 3 and 4
Empigen® BS/FA
Competitor B
Binary system using Pureact WS Conc + CAPB increases formulation viscosity
Topped fatty acid CAPB provides higher viscosities at lower concentrations of sodium chloride compared to ‘oil derived’ CAPB
Choice of CAPB grade is important: Stripped/topped fatty acid based CAPBs give the highest viscosity compared to triglyceride oil based CAPBs
Electrolyte Thickening of Pureact WS Conc/CAPB Systems

## Slide 20: 10% Active Iselux® and Cocamidopropyl Hydroxysultaine
Chart: NaCl / %w/w
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8
2% CAPHS | 0 | 0 | 500 | 960 | 1460 | 1880 | 1960 | 1980 | 1540
4% CAPHS | 800 | 2140 | 4360 | 5890 | 5540 | 4180
6% CAPHS | 15860 | 14000 | 10060
pH 5.8

## Slide 21
Chart: NaCl / % w/w
| 0 | 0.4 | 0.8 | 1.2 | 1.6 | 2 | 2.4 | 2.8 | 3.2 | 3.6 | 4 | 4.4000000000000004
Empigen BS/FA | 0 | 50 | 125 | 440 | 1550 | 4970 | 9980 | 14740 | 19450 | 22200 | 23500 | 23100
Empigen BB | 0 | 940 | 3540 | 9800 | 16420 | 18940 | 14840
Empigen CDL 60P | 0 | 44 | 86 | 236 | 700 | 1410 | 4290 | 6980 | 9820 | 10620 | 7780
Empigen CDR 60 | 0 | 34 | 55 | 108 | 335 | 734 | 1002 | 2580 | 5650 | 9480 | 10540 | 7650
Empigen 5151 | 0 | 50 | 150 | 440 | 1255 | 3670 | 7370 | 8400 | 5840
Electrolyte Thickening of Nansa® LSS 38/AV
with amphoteric surfactants
9%w/w Active Sodium C14-C16 Olefin Sulfonate, 3%w/w Active amphoteric, pH 5.0
Lauryl Betaine
Sodium lauroamphoacetate
Sodium cocoamphoacetate
Disodium Cocoamphodiacetate

## Slide 22: Foam textures with Pureact WS Conc Effect of co-surfactants
Pureact WS Conc & CAPB
Pureact WS Conc & CAPB & Pureact LSR
Pureact WS Conc & CAPB & Iselux®
Pureact WS Conc & CAPB & Gluco L

## Slide 23: Conditioning Agents with Pureact WS Low pH
Adding high levels of salt can cause the separation of cationic polymers (complex coacervate)
Worse effect at low pH
Adding co-surfactants helps – lower salt levels needed to thicken
Coacervate formed of PQ 10 and anionic surfactant, ‘salted’ out of formulation (45°C)
5% SMCT, 4.5% CAPB, 0.2% PQ-10
NaCl q.s. to 5,000cps

## Slide 24: Effect of surfactants on stability and clarity Cationic polymers at low pH
INCI | Trade Name | % w/w |  |  |  |  | 
 |  | A | B | C | D | E | F
Aqua |  | q.s. to 100 | q.s. to 100.0 | q.s. to 100 | q.s. to 100 | q.s. to 100 | q.s. to 100
Polyquaternium-10 | Polyquta 400 KC (KCI Limited) | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Sodium Methyl Cocoyl Taurate | Pureact WS Conc (Innospec) | 21.3 | 7.2 | 7.2 | 7.2 | - | 7.2
Sodium Lauroyl Methyl Isethionate | Iselux® (Innospec) | - | - | - | - | - | 2.0
Lauryl Glucoside | Pureact Gluco L (Innospec) | - | - | - | 3.6 | - | 3.0
Sodium Methyl Oleoyl Taurate | Pureact MS-CG (Innospec) | - | 3.6 | 3.6 | 3.6 | 3.6 | 3.6
Sodium C14-C16 Olefin Sulfonate | Nansa® LSS 38 / AV (Innospec) | - | 8.33 | 8.33 | 3.8 | 10.5 | -
Cocamidopropyl Betaine | Empigen® BS/H50 (Innospec) | 10 | 10 | - | - | - | 10
Cocamidopropyl Hydroxysultaine | Surfac SB09 (Surfachem) | - | - | 9.4 | 9.4 | 9.4 | -
Sodium Benzoate |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
Citric acid 50%w/w |  | q.s.to pH 4.5 | q.s.to pH 4.5 | q.s.to pH 4.5 | q.s.to pH 4.5 | q.s.to pH 4.5 | q.s.to pH 5.5
Formulations contain 10.0% w/w total active surfactant

## Slide 25
Achieving clarity in sulfate-free surfactant systems containing PQ-10
Sample A
Pureact WS Conc (SMCT), Empigen BS/FA (CAPB)
NaCl / %: (0, 0.4, 2.0, 2.5, 3.0, 4.0)
Sample B
Pureact WS Conc (SMCT), Nansa LSS 38/AV (AOS), Pureact MS-CG (SMOT), Empigen BS/FA (CAPB)
NaCl / %: (0, 0.4, 0.8, 1.2, 1.6, 2.0)
Sample C
Pureact WS Conc (SMCT), Nansa LSS 38/AV (AOS), Pureact MS-CG (SMOT), Cocamidopropyl hydroxysultaine
NaCl / %: (0, 0.4, 0.8, 1.2, 1.6, 2.0)
Sample D
Pureact WS Conc (SMCT), Pureact Gluco L (Lauryl Glucoside), Nansa LSS 38/AV (AOS), Pureact MS-CG (SMOT), Cocamidopropyl hydroxysultaine
NaCl / %: (0, 0.4, 0.8, 1.2, 1.6, 2.0)
Sample E
Nansa LSS 38/AV (AOS), Pureact MS-CG (SMOT), Cocamidopropyl hydroxysultaine, NaCl / %: (0, 0.4, 0.8, 1.2, 1.6, 2.0)
Sample F
Pureact WS Conc (SMCT), Iselux (SLMI), Pureact Gluco L (Lauryl glucoside) Pureact MS-CG (SMOT), Empigen BS/FA (CAPB),
NaCl / %: (0, 0.4, 0.8, 1.2, 1.6, 2.0)

## Slide 26: Formulations A-F viscosity Clarity with NaCl
NaCl level at which loss of clarity occurs
Chart: NaCl / %w/w
| 0 | 0.4 | 0.8 | 1.2 | 1.6 | 2 | 2.4 | 3 | 3.5 | 4
A | 0 | 0 | 0 | 0 | 0 | 490 | 1860 | 4260 | 6240 | 8290
B | 0 | 330 | 1820 | 4530 | 8060 | 8280 | 8300
C | 0 | 100 | 350 | 1180 | 3160 | 7280 | 7860
D | 940 | 2520 | 4660 | 6480 | 7400 | 7800 | 8400
E | 510 | 3000 | 6300 | 8820 | 11000 | 12400 | 12160
F | 50 | 300 | 1450 | 4500 | 9500 | 10940 | 9100
Viscosity Brookfield RVT, 20 rpm # 2, 3 and 4
Approximate region of optimum stability, clarity and viscosity
(From previous slide)

## Slide 27: Example formulations
From Innospec

## Slide 28
H0105 naturally mild conditioning shampoo
INCI ingredients | Trade name (supplier) | % w/w
A. Aqua |  | q.s to 100.00
Polyquaternium-10 | Polyquta 400 KC (KCI Limited) | 0.20
B. Sodium Methyl Cocoyl Taurate | Pureact WS Conc. (Innospec) | 9.40
Lauryl Glucoside | Pureact Gluco L (Innospec) | 3.60
Sodium Methyl Oleoyl Taurate | Pureact MS-CG (Innospec) | 3.60
Sodium Lauroyl Sarcosinate | Pureact LSR (Innospec) | 1.35
C. Cocamidopropyl Hydroxysultaine | Surfac SB09 (Surfachem) | 9.40
D. Sodium Benzoate |  | 0.50
E. Fragrance | Pomette (Azur Fragrances) | 0.50
F. Citric Acid (50% w/w) |  | q.s.to pH 4.2-4.7
G. Sodium Chloride |  | q.s. to 4,500-8,000cps (max 0.8%)
Properties | 
Appearance: | Clear, viscous liquid
pH: | 4.2 – 4.7
Viscosity*: | 8,000 – 11,000 cPs
 | *Brookfield RV, # 5 @20 rpm, 20ºC
Crystal clear formulation
Only NaCl thickened no rheology modifier needed

## Slide 29: Sustainable formats in-cosmetics 2019

## Slide 30
S0214 Charcoal
Cleanse and
Shave Stick
S0216 Bubble Scrub Butter
S0202 Powder-to-Foam
Facial Cleanser
Sustainable formats

## Slide 31
H0110 ‘Small but Mighty’
Shampoo Butter
AC 319 Charcoal
Shampoo Bar
Sustainable formats

## Slide 32
H0113 Hair There and Everywhere
Compacted Shampoo Bar
Iselux® SCMI
H0109 Powder-to-Foam Sprinkle
& Shine Shampoo
Pureact WSP, Pureact I-78, Pureact SCG and Activsoft C-13
S0211 ‘Discover Green’ Body Cleanser
Pureact WS Conc, Pureact Gluco L, Pureact MS-CG, Pureact LSR and Empigen® BS/FA – 95% Naturally Derived by ISO 16128
S0221 Cleansing Stick
Iselux® SCMI
Sustainable formats

## Slide 33
Gently Exfoliating Shower Gel
S0179
Micellar water
S0178
Shake, Shower and Shave Shower Gel
S0168
Trio of Oils Hair and
body Wash
S0128
Bubble Scrub Butter
S0132a
Intensive care Argan oil cream shampoo
H0060
Good to Go,
Shampoo Bar
H0061
Zesty Sorbet Scrub
S0119a
Transparent Luxury Cleansing Bar
For Face and Body
S0152
Ultra Mild Baby Bath Cleanser
AC235
Interesting Formulations and Textures with Iselux®
Bubblegum Jelly Wash
S0172

## Slide 34: Summary
Innospec are experts in sulfate-free formulating with world class popular surfactants.
We have overcome many of the challenges in sulfate-free formulating, optimising formulations to specific briefs to achieve:
  Desired foaming performance
  Stability
  Viscosity with salt thickening or rheology modifiers
  Clarity (or opacity)
  Conditioning
We have a library of stable guide formulations which you can use as-is or as bases for your product development.
We can help you develop high-performing systems according to your briefs.
Please contact us to discuss how we can work together.
How to optimise formulations when using modern preservatives by careful choice of the surfactants used
  Achieving stability
  Achieving viscosity
  Achieving clarity

## Slide 35: thank you for listening
please visit Innospec stand H88 for more information
tony.gough@innospecinc.com